## Slide 1: TRANSISTOR BIASING

## Slide 2
•Transistor is a solid state device whose operation depends upon the flow of electric charge carriers within the solid.
•Current controlled device
•Transistor is called BJT
APPLICATION
•Control system
•Satellites and Mobile phones
•Communication System
ADVANTAGE
•Compact Size
•Light weight
•More resistive to shock and vibrations
•Low operating Voltage
•High Operating Efficiency

## Slide 3
JUNCTIONS
•Emitter Base Junction
•Collector Base Junction
TERMINALS
•Emitter - heavily doped. Supply majority charge carriers.
•Base – lightly doped. Pass most of the carriers into collector
•Collector –moderately doped. Collect majority carriers.
The FBed EB Jun offers low resistance to emitter current whereas CB jun which is RBed offers High resistance to collector current.

## Slide 5: NEED FOR BIASING
The purpose of DC biasing of a transistor is to obtain certain DC collector current at a certain DC collector voltage in order to produce distortion free output.
The values of current and voltage are named as Q point or Quiescent point or DC conditions
A transistor can be biased with the help of battery.

## Slide 6: TRANSISTOR LOAD LINES
It is the line on which the operating point moves when AC signal is applied to the transistor.
Apply KVL on o/p section
Vcc = IcRc+ VCE ------(1)
VCE = Vcc-IcRc -----(2)
Ic = Vcc-VCE
Rc
When Vce = 0 , Ic = Vcc/Rc from eqn(1)
Ic = 0 Vce=Vcc

## Slide 7
If we join two points A & B , DC load line is obtained.
Q point:-It is apoint on the dc load line which
represents dc collector emitter voltage Vce and
collector current Ic in the absence of AC signal.

## Slide 9: Stabilization
Only the fixing of a suitable operating point is not sufficient but it is also to be ensured that the operating point remains stable.
It does not shift due to change in temperature or due to variations in transistor parameters.
The maintenance of the operating point stable is known as stabilization

## Slide 10: FACTORS RESPONSIBLE FOR SHIFT IN Q POINT
There are two reasons for the operating point to shift
The transistor parameters are temperature dependent.
The parameters (such as β) change from unit to unit

## Slide 11: FACTORS RESPONSIBLE FOR SHIFT IN Q POINT
Temperature dependence
Flow of current in the collector circuit produces heat at the collector junction and this increases the temperature.
More minority carriers are generated in base-collector region and then the leakage current ICBO increases
When ICBO increases, then ICEO also increases, which in turn increase the collector current. This further raises the temperature of the collector – base junction and the whole cycle repeats again.
The excess heat produced at the junction may even burn the transistor. This situation is known as thermal runaway.

## Slide 12
β dependence
If we replace the transistor then due to variations in β, collector current Ic will vary and hence operating point is shifted.
Requirements of a biasing circuit
To establish the operating point in the centre of active region of output characteristics so that operation of transistor always remains in active region with applied input signal.
To make the operating point independent of temperature variations.
To stabilize the operating point against transistor parameters

## Slide 13: STABILITY FACTOR
The rate of change of collector current IC with respect to the collector leakage current ICO at constant β and IB is called Stability factor.
Any change in collector leakage current changes the collector current to a great extent. The stability factor should be as low as possible so that the collector current doesn’t get affected. S=1 is the ideal value.

## Slide 15: METHODS OF TRANSISTOR BIASING
The commonly used methods of transistor biasing are
Fixed bias/Base Resistor method
Collector to Base bias
Biasing with Collector feedback resistor
Self bias/Voltage-divider bias
All of these methods have the same basic principle of obtaining the required value of IB and IC from VCC in the zero signal conditions.

## Slide 16: FIXED BIASING/BASE RESISTOR METHOD
In this method, a resistor RB of high resistance is connected in base, as the name implies. The required zero signal base current is provided by VCC which flows through RB. The base emitter junction is forward biased, as base is positive with respect to emitter.
The required value of zero signal base current and hence the collector current (as IC = βIB) can be made to flow by selecting the proper value of base resistor RB. Hence the value of RB is to be known. The figure below shows how a base resistor method of biasing circuit looks like.

## Slide 17
Apply KVL to input loop
Vcc-IBRB-VBE = 0
-IBRB = VBE - VCC
IB = VCC - VBE
RB
Since VBE is very small compared to VCC , VBE can be neglected
IB = VCC/RB Supply voltage Vcc being of fixed value. If RB is selected IB is also fixed. Hence the
IC= 𝛃Vcc …….(1) name fixed bias
RB

## Slide 18
Apply KVL to o/p loop
Vcc-IcRC-VCE = 0
VCE = Vcc - IcRC ……… (2)
Equation (1) and (2) determines Q point
The value of Ic and Vce depend on value of 𝛃 which depends strongly on temperature. So Q point will change with change in 𝛃 due to variation in temperature.
Equation 2 and 3 determines the Q point.
The value of Ic and Vce depend on value of

## Slide 19: Stability Factor for Fixed Biasing Circuit
In Fixed bias dIB/dIc = 0 because IB is independent of Ic.
S = 1+𝛃
Merits:
· It is simple to shift the operating point anywhere in the active region by merely changing the base resistor (RB).
· A very small number of components are required.

## Slide 20
Demerits:Why fixed bias is seldom used?
Any rise in temperature results in rise of ICBO and ICEO.Hence Ic rises resulting in increase in collector junction temperature. This is a cumulative process and the collector current goes on increasing. Therefore the operating point is not stable.
When the transistor is replaced with another one, considerable change in the value of β can be expected. Due to this change the operating point will shift.

## Slide 23: SELF BIAS OR VOLTAGE DIVIDER BIAS
It is a type of dc circuit in which the operating point is independent of transistor current gain 𝛃
The name voltage divider is formed by resistors R1 and R2 across Vcc.
RE provides stabilisation
The voltage drop across R2,forward biases the EB junction.
To find Q point(VCE,IC)
Assume that the base current IB is very small compared to the currents in R1 & R2
I1≈ I2 >> IB
If current flowing through R1 is I1, since IB is very small, then the current flowing through R2 can be assumed to be I1.
I1 = Vcc/(R1+R2)

## Slide 24
Voltage across R2 is VB = I1.R2 = Vcc R2
R1+R2
Apply KVL to base emitter loop
VB - VBE - VE = 0
VE = VB - VBE -------- (A)
Emitter current IE = VE/RE = VB - VBE
RE
Collector current IC⩰ IE = VB - VBE
RE ......... (1)
Apply KVL to collector side
Vcc - IcRc - VCE - IERE = 0
VCE = VCC - IC(RC+RE) ............. (2)
.

## Slide 25
From (1) AND (2) it is clear that Q point is independent of 𝛃. So this method is widely used
How RE provides excellent stabilization
From (A) VBE = VB - VE ........(3)
If Ic increases due to rise intemperature, the voltage drop emitter resistance RE increases. But the voltage VB = Vcc.R2
R1+R2 ie VB is independent of collector current, therefore VBE decreases (3) .
This will decrease the value of IE which inturn reduce the value of Ic to its original level . IC⩰ IE = VB - VBE
RE
Thus RE provides thermal stability.